European Style

Pen Assembly

- Choose your wood for your Pen Tubes.

- Cut 2 pieces ¾ x ¾ x 2 ½ inches.

- Drill 7mm hole through both pieces.

- Glue pen tubes into both pieces with ends being flush.  Use quick drying glue from Mr. K., being careful not to glue fingers together.

- Use Barrel trimming bit to remove excess glue and to bring both ends of wood pieces flush with pen tubes.

- Assemble pieces on mandrel according to picture below.

- Mr. K. will demonstrate Roughing Gouge and Skew Chisel tools for turning your pen.

- After finished turning your pen sand with a block starting with 80, 150, 240 and then end with 400 grit sandpaper.

- Apply Hut finish with Lathe off.

- Wait 5 minutes and apply second coat of Hut.

- Using a clean towel you will apply pressure on the pen buffing the Hut to a shine.

- Apply a coat of wax to pen and buff to gloss finish.

- Disassemble mandrel of pen pieces and return all parts to Mr. K.

- Mr. K will show you how to assemble your pen with vice clamp.

- Mr. K. will grade your pen before you take it home.